## Slide 1: Neural Networks for Scoliosis Quantification
Ben Church

## Slide 2: Content
Background
  Scoliosis
  Assessment
  Tracked ultrasound
Motivation
Methods
  Pre-processing
  Neural network
Results
Discussion
Ongoing work

## Slide 3: Background - Scoliosis
Pathological spinal curvature
Develops during growth
Must be monitored

## Slide 4: Background - Assessment
X-ray imaging is the gold-standard
Measure Cobb angle from X-ray, quantifying severity

## Slide 5: Background – Tracked ultrasound
Risks of cumulative X-ray exposure have motivated use of 3D ultrasound
Provides landmark locations rather than macroscopic visualization
Curvature extracted from landmark locations

## Slide 6: Motivation
3 expected error types:
Missing points
Misplaced points
Random noise
Can curvature be retrieved?

## Slide 7: Methods – Pre-processing

## Slide 9
Feedforward backpropagation network
Curvature estimate

## Slide 10: Methods – Neural network

## Slide 11: Results
Chart: Noise Standard Deviation (mm2)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Testing Mean Absolute Error | 19.2394 | 21.7401 | 19.2428 | 21.0865 | 27.5353 | 25.4982 | 26.785 | 23.9578 | 25.7127 | 28.1354 | 27.0401
Training Mean Absolute Error | 7.7914 | 9.8834 | 6.3676 | 4.6187 | 10.5138 | 10.8801 | 5.9757 | 9.2442 | 5.338 | 8.72 | 9.2446

## Slide 12: Discussion
Accuracy is unimpressive
  Small training set
MATLAB results are uninformative
  Does not indicate curve severity vs performance relationship

## Slide 13: Ongoing work
Use neural network to estimate Cobb angle defining vertebrae
  Alternative to direct angle estimation
Create method to repair missing points

## Slide 14: Thank you! Questions?