## Slide 1
Spine visualization from transverse process landmarks
Methods
Registration of a generic anatomical model was tested in 5 CT scans with spinal deformities
Transverse processes are marked in both patient and generic anatomical model (red points in Fig 2)
Anchor points are automatically added to constrain in anterior extent and rotation of vertebra models
Thin-plate spline transformation was applied on spine model based on landmarks and anchor points
Results
Conclusion
The method produces spinal visualization similar to CT segmentations. It is sufficiently robust to deal with scoliotic anatomy. The method can also be adapted to other imaging modalities; visualizations can be generated from symmetric landmarks, whatever modality is used to locate them
Acknowledgement
This work was made possible by funding from: Province of Ontario; Cancer Care Ontario with funds from the Ministry of Health; Long-Term Care for an Applied Cancer Research Unit; Research Chair in Cancer Imaging; Natural Sciences and Engineering Research Council of Canada under the Discovery Grants program and Canadian Graduate Scholarship.
Objective
Visualize full spinal anatomy of patients with spinal deformities using ultrasound-accessible landmark localizations (transverse processes) as the only input for visualization
Ben Church, Andras Lasso, Christopher Schlenger, Daniel P. Borschneck, Parvin Mousavi, Gabor Fichtinger, Tamas Ungi
Queen’s University, Kingston, Canada
Reference
Registrations were generated for 5 scoliotic patients and compared to CT segmentation ground-truth
Average and maximum Hausdorff distances were computed
Registration to ground-truth distances were computed and represented as error maps
Ungi T et al. Spinal curvature measurement by tracked ultrasound snapshots. Ultrasound in medicine and biology. 2014 Feb;40(10):447-545.
Introduction
Spine anatomy is complex, and some diseases cause spine deformities
Pathological spine curvatures are often visualized by X-ray, CT, or MRI
The problem with CT and X-ray is radiation exposure, while MRI has limited availability and high cost
Ultrasound is a safe, inexpensive, and widely accessible alternative imaging modality
Spine landmarks, such as transverse processes can be localized in ultrasound (Ungi et al. 2014)
Spinal curvatures can be measured from ultrasound landmarks (Fig 1)
Fig 1. Series of ultrasound snapshots for locating transverse processes, with curvature angle illustrated in red
Patient # | Avg. Hausdorff (mm) | Max. Hausdorff (mm)
1 | 2.8 | 20.0
2 | 2.3 | 24.0
3 | 2.4 | 17.7
4 | 2.9 | 18.1
5 | 3.3 | 23.8
Fig 2. Transverse processes (red), and additional anchor points (green)
Fig 3. Registration computes transforms displacing model points to patient’s
Fig 5. Registrations compared to CT-derived patient ground-truth. Error map shows distance between surfaces
Fig 4. Thin-plate spline interpolation of healthy model to patient anatomy